## Slide 1: Component Test Streamlining
Renew Test Handling
By
DCVI

## Slide 2: Challenges of current copy strategy
Feature | Problem
Large number of copies Same/Similar code(libs) in every variant | Time consuming rework for generic changes Fixes in variants not easily distributed Features variant specific behavior
No overview across Variant/Option/Feature/Test/Result | Missing or not executed tests are not identified Duplicated test cause effort and execution time
Variant development overlap with each other and dcvi | Risk of missing transfer (requires manual tracking) Requires time consuming sync between variants Triggers merge conflicts
Increasing number of maintained variants | Test maintenance effort grows every year Slows down/prevents feature development due to large effort for test adaption
Fixes or improvement of coverage | Test fixes required due to CR’s are difficult to distribute or find across variants Distribution of coverage improvements are time consuming and difficult to do within the timeframe of a CR

## Slide 3: Current Test Variants
Style | Pro | Con
Copy per variant | Fully independent No merge conflicts Fast initial development | Time consuming maintenance Requires effort to sync Duplicates will be copied and worst case another duplicate added
Common test which loop across variants | Fast development of new variant “Same” coverage across variants No/low sync effort across variants | Grow very fast very big Difficult to adapt for variant specific features Variant might be added without understanding of test/expect Difficult to document Variant specific expect in common location

## Slide 4: Requirements for future Component Testing
Requirement | Benefit | Risk
No Copies | Easy to maintain Single source for test logic can/must be better documented Features same behavior across variants (Reuse triggers intense review) | Merge conflicts Updates may disturb original test Larger effort due to more complex test caused by variant features
Centralized overview of test results/coverage displaying test/variant/option/feature/result(P/F/S/NA) | Known coverage Clear test target | 
Overview tests which enabled subComponent tests in case of fail | Save execution time in case of pass Details for debugging in case of fail | Test gaps due to missing coverage in overview test. (To avoid test gaps run “debugging” tests e.g. weekly)
Measurement data collection testId/analogResult/<P/F/S/NA> | Simplify root cause analysis | Large amount of data
Support of complex test sequences with flexible/simple access to atomic checks (logset/state data/…) | Reduce overall number of tests as, one sequence can do multiple checks. | Increase complexity
Standard setups (Typical/Min/Max/…) | Simplifies new variant setup Minimizes maintenance effort | May end up with large number of “Standards” Reduced test coverage due to “same” values all over the place
Variant specific data must be in variant | Clear correlation of test data location and variant | 
Test must be started from variant | No need-to-know which tests to execute | 
Test need to be executable via bazel test | Flexible test execution (General features of professional test framework) | 
Categorize tests e.g. basic/smoke tests/special tests | Supports flexible test flows Shorten test execution | 

## Slide 5: Building Blocks
Test Setup
Test Execution
Time/Release/Workspace Based Atomic results
Test Analysis
Variant List
Setup Collection
Typ/Variant/option
Test Collection
Feature/Logic/AtomicCheck
Test Id
Test Result Table
Unique Id (variant/feature) / Result(P/F/S/E/NA/-)
Test Measurement Table
Unique Id (variant/feature)
Atomic Result (Analog measurement/state/logSet data
???
Variant Ids
Unique Ids
?Spec values? (Typ/MinRange / MaxRange)
Instrument Collection
(Pin Config)

## Slide 6: Execution Blocks
Test Executor
What to test
Variant / Option / PinConfig List
Setup Collection
Typ/Variant/option (or NA) Set of attributes like level action/parameter/sequence(?)
Test Collection
Feature/Logic/AtomicChecks
Test Result log
Unique Id (variant/feature) / Result(P/F/S/NA/-)/Atomic Result (Analog measurement/state/logSet data( *Size?)
Instruments
Test Generation
Per Instrument
Test Execution
(Plain Code)

## Slide 7: Dcvi Test Execution Configuration
Id | Group | Name | Features/FeatureId | AVI64 |  |  | FVI16 |  |  | 
 |  |  |  | AVI64_None_Single_1 | AVI64_None_Gang_1_2 | AVI64_None_Gang_7_8 | FVI16_None_Stack_1_2 | FVI16_None_Stack_7_8_9 | FVI16_highVoltage_Single_1 | FVI16_None_Single_1
1000 | Level | Simple | Connect via levels Force voltage Involved states are correct | A | A | F | A | F | A | A
++ |  | Vmeas | Connect via levels Force voltage Measure voltage | A | A | F | A | F | A | A
++ |  | Profiling | Connect via levels Force voltage Profile voltage | F | A | F | A | F | F | F
++ |  | Debug | Complete Power Sequence | D | S | S | D | S | S | D
Execution Scenario:
Goals
shorten execution time by limiting test coverage
Skip time consuming tests with special focus
Quickly enable debug test without recompile e.g. fail cases
Support of debug/implementation configurations
A = Always
F = Only for Full coverage
NA = Not Applicable
S = Skip
D = Debugging

## Slide 8: Dcvi Instrument Configuration
Variant | Option | PinType | PinNumber | Alias(back Reference?)
AVI64 | None | Single | 1 | AVI64_None_Single_1
 |  | Gang | 1,2 | AVI64_None_Gang_1_2
 |  |  | 7,8 | AVI64_None_Gang_7_8
FVI16 |  | Single | 1 | FVI16_None_Single_1
 |  | Stack | 1,2,3 | FVI16_None_Stack_1_2
 |  |  | 7,8,9 | FVI16_None_Stack_7_8_9
 | highVoltage | Single | 1 | FVI16_highVoltage_Single_1

## Slide 9: Dcvi Instrument Setup
InstrumentName | Attribute | Generic | AVI64 | FVI16 | 
 |  | (All Variants) | Generic | Generic | highVoltage
pin1 | Level.vforce | forceVal |  |  | 
 | Level.iclampSource | clampHigh | clampHigh * gangCount | 0.5 * gangCount | 0.01
 | Level.iclampSink | clampLow | clampLow * gangCount | 0.5 * gangCount | 0.01
 | Level.irange | irange | - |  | 0.02
 | Level.vrange | vrange | vrange | 10.0 | 65.0
 | Level.settling | 0.001 | 0.001 | 0.001 | 
 | Expect.States.irange | 0.2 | 0.2* gangCount | gangCount>1?3.0* gangCount:irange | 
VariableName | Value
forceVal | 1
clampHigh | 0.03
clampLow | 0.03
irange | 0.033 * gangCount
vrange | 3.0
SetupName = Normal

## Slide 10: Decisions
Reason | Decision
Need to prevent excessive/uncontrolled feature set | Limit judges to check bool/enum/measresults against limits Support of one variant in test template
Avoid complicated hierarchy Have transparent setups | Test templates(function) will be in common location Reuseable code(Create measurement façade/judge) shall be located in common location Executable cpp code will be in variant location Parameters shall be in plain cpp code

## Slide 11: Dcvi Test Setup TestName = Level:Simple
Input: uniqueId, instrument, setupAndExpect
Measurement = createMeasurement(„pin1“, instrument);
Measurement .getAndApplySetup(„pin1“, instrument, setupAndExpect); // apply setup pin1
checkAndLog (uniqueId, „Build result“, /*expect*/ OK, Measurement .build());
checkAndLog (uniqueId, „Execute result “, /*expect*/ PASS, Measurement .execute());
checkAndLog (uniqueId, „State checks “, /*expect*/ setupAndExpect.expect.State);

## Slide 12: Next Steps
Prove of concept:
Manually setup required files in required location
  Common data
    test template in hw/ext/tests/templates (?)
    test execution configuration in hw/ext/tests/execution (?)
    Test setup definition(Setups including generic setup, which might work for large number of variants)
  Variant data in hw/ext/<variant>/Driver/TestSetups(?)
    Instrument configuration
    Instrument setup
Prepare generator to generate a working component test based on the manual files
Prepare GUI interfaces to write json input files
  Instrument definition
  Flow definition
  Test setup definition
  …
Provide GUI for fast and failure preventing setup
Read instrument model (on demand – e.g. generate min max setups/use defaults)
Assist creation of new variants

## Slide 13: Notes:
Variant specific data shall be in variant -> generic test directory with variant specific setup/expect not acceptable